## Slide 1
الجامعة السعودية الالكترونية
الجامعة السعودية الالكترونية
26/12/2021

## Slide 2
College of Computing and Informatics
Computer Science Program
CS231
Digital Logic Design

## Slide 3
CS231
Digital Logic Design
Module 02: Boolean Algebra and Logic Gates

## Slide 4
Binary Codes
Binary Storage and Registers
Binary Logic
Axiomatic Definition of Boolean Algebra
CONTENTS

## Slide 5
Weekly Learning Outcomes
Gain a basic understanding of postulates used to form algebraic structures.
Understand the basic theorems and postulates of Boolean algebra
Know how to apply DeMorgan’s theorems

## Slide 6
Required Reading
Chapter 1, and 2
(Digital Design with An Introduction to the Verilog HDL, VHDL and System Verilog)
Recommended Reading
Chapter 2 (Digital Logic for Computing) (John Seiffertt Digital Logic for Computing)
This Presentation is mainly dependent on the textbook: Digital Design with An Introduction to the Verilog HDL, VHDL and System Verilog by Mano and Ciletti,

## Slide 7
Binary Codes

## Slide 8: Binary codes
Digital system signals have two distinct values only
Information in real world need more than two values to be represented more accurately
An n-bits binary code is a group of n bits that can have 2n distinct values
Numerical values can be represented by directly binary numbers using the conversion techniques we discussed in the class
Non-Numerical values, such as alphabet characters, needs a mapping between distinct bit-group values and the non-numerical values

## Slide 9: Non-numeric Binary Codes
Given n binary digits (called bits), a binary code is a mapping from a set of represented elements to a subset of the 2n binary numbers.
Example: A binary code for the seven colors of the rainbow
Code 100 is not used
Binary Number
000
001
010
011
101
110
111
Color
Red
Orange
Yellow
Green
Blue
Indigo
Violet

## Slide 10: Number of Bits Required
In the previous example (rainbow colors) we used 3 bits and one of the values is not used, can we use less bits for representation?
  The minimum number of bits depends on the number of elements to be represented.
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
  2n ≥ M > 2(n – 1)
  n = log2 M where x , is called the ceiling function, i.e., the integer greater than or equal to x.
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 11: Number of Bits Required (examples)
Example: How many bits are required to represent decimal digits with a binary code?
  M = 10, hence n = ceiling (log2 10) = ceiling (3.3219) = 4
  Checking:
Example: Given a machine with [off, low power, medium power, high power, ultra high power] states how many bits are required to represent these states?
  M = 5, hence n = ceiling (log2 5) = ceiling (2.32192) = 3
  Checking
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 12: Binary Codes
Group of n bits
  Up to 2n combinations
  Each combination represents an element of information
Binary Coded Decimal (BCD)
  Each Decimal Digit is represented by 4 bits
  (0 – 9)  Valid combinations
  (10 – 15)  Invalid combinations
Decimal | BCD
0 | 0 0 0 0
1 | 0 0 0 1
2 | 0 0 1 0
3 | 0 0 1 1
4 | 0 1 0 0
5 | 0 1 0 1
6 | 0 1 1 0
7 | 0 1 1 1
8 | 1 0 0 0
9 | 1 0 0 1

## Slide 13: Gray Code
Only one bit changes from one code to the next code
Less power consumed since less transistors go on and off.
Different than Binary
Binary
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Decimal | Gray
00 | 0000
01 | 0001
02 | 0011
03 | 0010
04 | 0110
05 | 0111
06 | 0101
07 | 0100
08 | 1100
09 | 1101
10 | 1111
11 | 1110
12 | 1010
13 | 1011
14 | 1001
15 | 1000

## Slide 14: Conversion or Coding?
Do NOT mix up conversion of a decimal number to a binary number with coding a decimal number with a BINARY CODE.
(13)10 = (1101)2 (This is conversion)
(13)BCD  (0001|0011)BCD (This is coding)
Advantages/Disadvantages?

## Slide 15: BCD: Advantages/Disadvantages
Disadvantage:
  It is obvious that a BCD number needs more bits than its equivalent binary value
    (26)10 = (11010)2
    (26)10 = (0010 0110)BCD
Advantages:
  Computer input/output data are handled by people who use the decimal system. So it is easier to convert back/forth to BCD.

## Slide 16: ASCII Code
American Standard Code for Information Interchange
Info | 7-bit Code
A | 1000001
B | 1000010
. . . | . . .
Z | 1011010
a | 1100001
b | 1100010
. . . | . . .
z | 1111010
@ | 1000000
? | 0111111
+ | 0101011
Each letter or symbol is assigned a number from 0 to 127.
For example the ASCII code for uppercase A is ‘1000001’ which is 65 decimal.

## Slide 18
Binary Storage and Registers

## Slide 19: Registers
A register is a group of binary cells. A register with n cells can store any discrete quantity of information that contains n bits.
The state of a register is an n‐tuple of 1’s and 0’s, with each bit designating the state of one cell in the register. for example, A 16‐bit register with the following binary content: 1100001111001001
A register with 16 cells can be in one of 216 possible states the register can store any binary number from 0 to 216 – 1.

## Slide 20: Transfer of Information among Registers

## Slide 21: Binary Transformation Processing

## Slide 22
Binary Logic

## Slide 23: Binary Logic
Binary logic deals with variables that take on two discrete values and with operations that assume logical meaning.
The two values the variables assume may be called by different names (true and false, yes and no, etc.), but for our purpose, it is convenient to think in terms of bits and assign the values 1 and 0.

## Slide 24: Binary Logic
There are three basic logical operations: AND, OR, and NOT. Each operation produces a binary result, denoted by z. 1. AND:
This operation is represented by a dot or by the absence of an operator. For example, x . y = z or xy = z is read “x AND y is equal to z.” The logical operation AND is interpreted to mean that z = 1 if and only if x = 1 and y = 1; otherwise z = 0. (Remember that x, y, and z are binary variables and can be equal either to 1 or 0, and nothing else.) The result of the operation x . y is z

## Slide 25: Binary Logic
2. OR:
This operation is represented by a plus sign. For example, x + y = z is read “x OR y is equal to z,” meaning that z = 1 if x = 1 or if y = 1 or if both x = 1 and y = 1. If both x = 0 and y = 0, then z = 0.

## Slide 26: Binary Logic
3. NOT:
This operation is represented by a prime (sometimes by an overbar). For example, x′ = z (or x̄ = z) is read “not x is equal to z,” meaning that z is what x is not. In other words, if x = 1, then z = 0, but if x = 0, then z = 1. The NOT operation is also referred to as the complement operation, since it changes a 1 to 0 and a 0 to 1, i.e., the result of complementing 1 is 0, and vice versa.

## Slide 27: Truth Table

## Slide 28: Logic Gates
Logic gates are electronic circuits that operate on one or more input signals to produce an output signal.

## Slide 29
Boolean Algebra

## Slide 30: Basic Definition
Boolean algebra, like any other deductive mathematical system, may be defined with a set of elements, a set of operators, and a number of unproved axioms or postulates.
A set of elements is any collection of objects, usually having a common property.

## Slide 31: Common Postulates
Closure
A set S is closed with respect to a binary operator if, for every pair of elements of S, the binary operator specifies a rule for obtaining a unique element of S.
For example, the set of natural numbers N = { 1 , 2 , 3 , 4 , … } is closed with respect to the binary operator + by the rules of arithmetic addition, since, for any a , b ∈ N , there is a unique c ∈ N such that a + b = c .

## Slide 32: Common Postulates
2. Associative law
A binary operator * on a set S is said to be associative whenever ( x ∗ y ) ∗ z = x ∗ ( y ∗ z ) for all x , y , z ∈ S
3. Commutative law
A binary operator * on a set S is said to be commutative whenever
x ∗ y = y ∗ x for all x , y ∈ S

## Slide 33: Common Postulates
4. Identity element
A set S is said to have an identity element with respect to a binary operation * on S if there exists an element e ∈ S with the property that e ∗ x = x ∗ e = x for every x ∈ S
Example: The element 0 is an identity element with respect to the binary operator + on the set of integers I = { … , - 3 , - 2 , - 1 , 0 , 1 , 2 , 3 , … } , since x + 0 = 0 + x = x for any x ∈ I The set of natural numbers, N, has no identity element, since 0 is excluded from the set.

## Slide 34: Common Postulates
5. Inverse
A set S having the identity element e with respect to a binary operator * is said to have an inverse whenever, for every x ∈ S , there exists an element y ∈ S such that x ∗ y = e Example: In the set of integers, I, and the operator + , with e = 0 , the inverse of an element a is ( - a ) , since a + ( - a ) = 0.

## Slide 35: Common Postulates
6. Distributive law
If * and ⋅ are two binary operators on a set S, * is said to be distributive over ⋅ whenever x ∗ ( y ⋅ z ) = ( x ∗ y ) ⋅ ( x ∗ z )
The operators and postulates have the following meanings: The binary operator + defines addition. The additive identity is 0 The additive inverse defines subtraction. The binary operator ⋅ defines multiplication. The multiplicative identity is 1. For a ≠ 0 , the multiplicative inverse of a = 1 / a defines division (i.e., a ⋅ 1 / a = 1 ).
  The only distributive law applicable is that of ⋅ over + : a ⋅ ( b + c ) = ( a ⋅ b ) + ( a ⋅ c )

## Slide 36
AXIOMATIC DEFINITION OF BOOLEAN ALGEBRA

## Slide 37: common postulates
In 1854, George Boole developed an algebraic system now called Boolean algebra.
For the formal definition of Boolean algebra, we shall employ the postulates formulated by E. V. Huntington in 1904.
Boolean algebra is an algebraic structure defined by a set of elements, B, together with two binary operators, + and ⋅ , provided that the following (Huntington) postulates are satisfied:

## Slide 38: Huntington Postulates
1. Closure 1. The structure is closed with respect to the operator + . 2. The structure is closed with respect to the operator ⋅ .
2. Identity element 1. The element 0 is an identity element with respect to + ; that is, x+ 0 = 0 + x = x . 2. The element 1 is an identity element with respect to ⋅ ; that is, x⋅ 1 = 1 ⋅ x = x .

## Slide 39: Huntington Postulates
3. Commutative 1. The structure is commutative with respect to + ; that is, x + y = y + x 2. The structure is commutative with respect to ⋅ ; that is, x ⋅ y = y ⋅ x
4. Distributive 1. The operator ⋅ is distributive over + ; that is, x ⋅ ( y + z ) = ( x ⋅ y ) + ( x ⋅ z ) 2. The operator + is distributive over ⋅ ; that is, x + ( y ⋅ z ) = ( x + y ) ⋅ ( x + z )

## Slide 40: Huntington Postulates
5. For every element x ∈ B , there exists an element x ′ ∈ B (called the complement of x) such that
x + x ′ = 1 and
x ⋅ x ′ = 0.
6. There exist at least two elements x , y ∈ B such that x ≠ y .

## Slide 41
Comparing Boolean algebra with arithmetic and ordinary algebra (the field of real numbers), we note the following differences:
1. Huntington postulates do not include the associative law. However, this law holds for Boolean algebra and can be derived (for both operators) from the other postulates. 2. The distributive law of + over ⋅ (i.e., x + ( y ⋅ z ) = ( x + y ) ⋅ ( x + z ) ) is valid for Boolean algebra, but not for ordinary algebra. 3. Boolean algebra does not have additive or multiplicative inverses; therefore, there are no subtraction or division operations.

## Slide 42
4. Postulate 5 defines an operator called the complement that is not available in ordinary algebra.
5. Ordinary algebra deals with the real numbers, which constitute an infinite set of elements. Boolean algebra deals with the as yet undefined set of elements, B, but in the two-valued Boolean algebra defined next (and of interest in our subsequent use of that algebra), B is defined as a set with only two elements, 0 and 1.

## Slide 43
Two-Valued Boolean Algebra

## Slide 44: Two-Valued Boolean Algebra
A two-valued Boolean algebra is defined on a set of two elements, B = { 0, 1 } , with rules for the two binary operators + and ⋅
These rules are exactly the same as the AND, OR, and NOT operations

## Slide 45: Two-Valued Boolean Algebra
We now show that the Huntington postulates are valid for the set
B = {0, 1} and the two binary operators + and .
That the structure is closed with respect to the two operators is obvious from the tables, since the result of each operation is either 1 or 0 and 1, 0 ∈ B.
From the tables, we see that (a) 0 + 0 = 0 0 + 1 = 1 + 0 = 1; (b) 1 . 1 = 1 1 . 0 = 0 . 1 = 0. This establishes the two identity elements, 0 for + and 1 for . , as defined by postulate 2.
The commutative laws are obvious from the symmetry of the binary operator tables.

## Slide 46: Two-Valued Boolean Algebra

## Slide 47: Two-Valued Boolean Algebra
5. From the complement table, it is easily shown that (a) x + x' = 1, since 0 + 0' = 0 + 1 = 1 and 1 + 1' = 1 + 0 = 1 (b) x . X' = 0, since 0 . 0' = 0 . 1 = 0 and 1 . 1' = 1 . 0 = 0 Thus, postulate 1 is verified.
6. Postulate 6 is satisfied because the two‐valued Boolean algebra has two elements, 1 and 0, with 1 ≠ 0.

## Slide 48
Thank You