## Slide 1
الجامعة السعودية الالكترونية
الجامعة السعودية الالكترونية
26/12/2021

## Slide 2
College of Computing and Informatics
Computer Science Program
CS231
Digital Logic Design

## Slide 3
CS231
Digital Logic Design
Module 03: Boolean Expression & Simplification

## Slide 4
Basic Theorems and Properties of Boolean Algebra
Boolean Expression
Logic Gates
Boolean Expression Simplification
CONTENTS

## Slide 5
Weekly Learning Outcomes
Define Boolean functions/Boolean expression
Learn how to express a Boolean function in canonical and standard forms
Learn the logic gates symbols and their truth tables
Learn how to manipulate Boolean expression to reduce the required number of logic gates

## Slide 6
Required Reading
Chapter 2
Chapter 3
(Digital Design with An Introduction to the Verilog HDL, VHDL and System Verilog)
Recommended Reading
Chapters 3 & 4 (John Seiffertt Digital Logic for Computing)
https://www.tutorialspoint.com/digital_circuits/digital_circuits_canonical_standard_forms.htm

## Slide 7
Basic Theorems and Properties of Boolean Algebra

## Slide 8: Basic Theorems

## Slide 9: Basic Theorems
The postulates are basic axioms of the algebraic structure and need no proof. The theorems must be proven from the postulates. Proofs of the theorems with one variable are presented next.

## Slide 10: Basic Theorems

## Slide 11: Basic Theorems

## Slide 12: Basic Theorems

## Slide 13: Basic Theorems
Therefore, since the complement is unique, we have (x')' = x. The theorems involving two or three variables may be proven algebraically from the postulates and the theorems that have already been proven.

## Slide 14: Basic Theorems

## Slide 15: Basic Theorems
The theorems of Boolean algebra can be proven by means of truth tables. In truth tables, both sides of the relation are checked to see whether they yield identical results for all possible combinations of the variables involved. The following truth table verifies the first absorption theorem:

## Slide 16: Basic Theorems

## Slide 17: Operator Precedence
The operator precedence for evaluating Boolean expressions is (1) parentheses, (2) NOT, (3) AND, and (4) OR. In other words, expressions inside parentheses must be evaluated before all other operations. The next operation that holds precedence is the complement, and then follows the AND and, finally, the OR.

## Slide 18: Boolean Functions
An algebraic function is an evaluation of a set of variables and operations
  F(x, y) = x + 2*y (variables F, x, y; operations +,*, =)
Boolean algebraic functions use logic operations only
Boolean variables values and function’s values can be 1, or 0
Example:
  Function:
  Variables:
  Boolean Expression:
  Logical Operations:
OR
NOT
AND

## Slide 19: Logic Diagram  Boolean Expression
Logic Diagram
What is the Boolean expression?
Y’
Y’.Z
X + Y’.Z
Evaluate from Inputs to Outputs

## Slide 20: Boolean Expression  Logic Diagram
Consider function
How many gates do we need to implement this function?
3-input AND Gate
2-input AND
OR Gate
First AND gate
Second AND gate
Third AND gate

## Slide 21: Truth Tables
A truth table spells all input combinations and their corresponding outputs
The rows of the table (number of combinations) depends on the number of variables
  For n variables we have rows
3 input variables

## Slide 22: Boolean Expression Truth Table
Derive the Truth Table.
X | Y | Z | Y’ | Y’Z | F
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
Input Variables
Boolean Expression

## Slide 23: Boolean Expression  Truth Table
X | Y | Z | Y’ | Y’Z | F
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
Y’
Y’Z
First Get the expression of the intermediate variables

## Slide 24: Boolean Expression  Truth Table
X | Y | Z | Y’ | Y’Z | F
0 | 0 | 0 | 1 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 0 |  | 
0 | 1 | 1 | 0 |  | 
1 | 0 | 0 | 1 |  | 
1 | 0 | 1 | 1 |  | 
1 | 1 | 0 | 0 |  | 
1 | 1 | 1 | 0 |  | 
Y’
Y’Z
We get the values of

## Slide 25: Boolean Expression  Truth Table
X | Y | Z | Y’ | Y’Z | F
0 | 0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 1 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 1 | 0 | 0 | 
1 | 0 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 0 | 
1 | 1 | 1 | 0 | 0 | 
Then the values of
Y’
Y’Z

## Slide 26: Boolean Expression  Truth Table
X | Y | Z | Y’ | Y’Z | F
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1
And finally, the value of the function
Y’
Y’Z

## Slide 27
Logic Gates

## Slide 28: Common Logic Gates and Expressions

## Slide 29: Boolean Operator Precedence
The order of evaluation in a Boolean expression is:
Consequence: Parentheses appear around OR expressions
Example: F = A(B + C)(C + D)
Parentheses 2. Not
3. And 4. Or

## Slide 30
Compliment of functions

## Slide 31: Complement of a Function
X | Y | Z | F | F
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1
The complement representation for a function F, (F’), is obtained from an interchange of 1’s to 0’s and 0’s to 1’s for the values of F in the truth table.

## Slide 32: Complement of a Function … Cont.
The complement of a function can be derived algebraically by applying DeMorgan’s theorem.
Complement the left hand side and the right hand side by putting a bar on top of each.

## Slide 33: Complement of a Function … Cont.
Yet another way of deriving the complement of a function is to:
  Take the dual of the function equation
  Complement each literal.

## Slide 34: Example (Why we need inverted input)
Chemical plant with the following properties
  Compound A
  Sensor detecting if temp > 300C
  Agent Z
Reactor is on only if
  Temp < 300 && compound A is used
  OR Agent Z is added with the mix

## Slide 35
Boolean Expression Simplification

## Slide 36: Representation: Truth Table
2n rows where n
is # of variables
Give Boolean Expression?
Not Simplified!
Can we do better

## Slide 37: Truth Table  Boolean Function
Let us first reconsider how to get a Boolean expression from a truth table
Consider a truth table
The Boolean expression for F:
  Sum or minterms (Oring of terms)
  Product of maxterms (Anding of terms)
What is a minterm?
What is a maxterm?

## Slide 38
Min Terms

## Slide 39: From Truth Table to Function
Consider a truth table
Can implement F by taking OR of all terms that are 1
MinTerm
Product Term

## Slide 40: Number of Minterms
For n variables, there will be 2n minterms
Like binary numbers from 0 to 2n-1
3-variables  8 minterms
X Y F
0 0
0 1
0
1 1
1
0
0
0
2-variables  4 minterms

## Slide 41: Product term
Assume we have a circuit with 3 input variables X, Y, Z
Definitions:
  Product Term – a subset of the variables appear (complimented or not with an AND operation between them)
   XY, XZ, XZ’, XYZ
  Min Term – is a product term in which all variables appear once  (XYZ, X’YZ, X’Y’Z’)
All min-terms are product terms but not all product terms are min terms

## Slide 42: Definition: Minterm
Is a Product Term in which ALL variables appear once (complemented or not)
One minterm active at a time

## Slide 43: Sum of Minterms (SOM)
OR all of the minterms of truth table row with a 1
In this case m1 + m3 + m4 + m6
In this case m0+m2+m5+m7
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 44: Alternative Representation
In this case m1 + m3 + m4 + m6
In this case m0+m2+m5+m7

## Slide 45: Summary of Properties of Minterms
There are 2n minterms for a Boolean function with n variables
Any Boolean function can be expressed as a logical sum of minterms
The complement of a function contains those minterms not included in the original function.
A function that includes all the 2n minterms is equal to logic 1.

## Slide 46
Sum of Products

## Slide 47: Sum of Products (SOP) Standard Form
The sum-of-minterms form is a canonical algebraic expression that is obtained directly from a truth table.
The expression obtained contains the maximum number of literals in each term.
Simplification of the sum-of-minterms expression is called sum-of-products.
  Simplified expression is called a standard form

## Slide 48: SOM vs. SOP
Sum of minterms (SOM)
After Simplification we get the Sum of products (SOP)

## Slide 49: Sum of Products Implementation
Sum of products
We refer to this implementation as a two-level circuit

## Slide 50: 2-level Implementation
Sum of products has 2 levels of gates
Is there a 3-level rep of this circuit?

## Slide 51: 2-level vs. 3-level Implementation
AB + CD + CE can be
Also expressed as
AB + C(D+E)
What’s best?
  Hard to answer!!
  More gate delays?
  But maybe we only have 2-input gates

## Slide 52
Thank You